## Slide 1: Analog and Digital Communication (ADC)
By Praveen Pawar
IIIT Bhopal
Last Updated: 2/28/2021 10:41 AM

## Slide 2: Preliminaries
Power
LTI System
Convolution
Convolution in time domain is equal to multiplication in frequency domain

## Slide 3: Preliminaries (continue…)
F. T.  Fourier Transform
 Impulse function
F. T.
F. T.
F. T.
F. T.

## Slide 4: Preliminaries (continue…)
Baseband Signal:
A baseband signal represents a low frequency signal having its lower cutoff frequency either zero or very close to zero.
0
Bandwidth,

## Slide 5: Preliminaries (continue…)
Bandpass Signal:
A bandpass signal represents a high frequency signal having its lower cutoff frequency very-very greater than zero.
Bandwidth,
Depending upon the relation between bandwidth and higher cutoff frequency, there are two types of bandpass signals.
Narrowband ()
Wideband
Where is the higher cut-off frequency of the message signal.
0
= higher cutoff frequency
– lower cutoff frequency

## Slide 6: Modulation Theorem (Fourier Transform)
F. T.
F. T.
F. T.
F. T.
Hilbert Transform
F. T.
F. T.

## Slide 7: Communication
Communication is the basic process of exchanging information.
A communication system essentially consist of three basic building blocks.
Transmitter
Channel
Receiver
Transmitter: - It is a physical system which transmits the information.
Receiver: - It is a physical system which receives the information.
Channel: - Channel is the medium through which information exchange takes place.
Depending upon type of channel used for information exchange, there are two types of communication:
1. Wireless Communication 2. Line or Wire Communication

## Slide 8: Modulation
Modulation is the process of superimposing the information content of a baseband modulating signal on a high frequency carrier signal by altering its characteristics (Amplitude, Frequency, and Phase).
Modulation process transmits low frequency baseband signal into a high frequency bandpass signal.
-> angular frequency in rad/sec.
-> natural frequency in Hz
Amplitude
Phase

## Slide 9: Need for Modulation
Avoids mixing of the signals
Allows multiplexing of the signals
Reduces height of the antenna
Increases range of communication
Increases quality of reception

## Slide 10: Amplitude Modulation (AM)
In time domain
  In amplitude modulation, the amplitude of high frequency carrier signal is varied in accordance with the instantaneous value of the baseband modulating signal keeping frequency and phase constant.
In frequency domain
  In amplitude modulation, the low frequency baseband signal is translated into high frequency bandpass signal.

## Slide 12: Equation for AM
Let, arbitrary modulating signal with maximum frequency
Carrier
signal
Message
signal

## Slide 13: AM: Frequency domain representation
0
0
1
½
LSB
USB
LSB = Lower Side Band
USB = Upper Side Band

## Slide 14
The AM signal contain three components, i.e., carrier signal, upper sideband (USB), and lower sideband (LSB).
The information is contained simultaneously in USB as well as LSB. The carrier does not contain any information.
The transmission bandwidth of AM signal is twice the maximum modulating signal frequency, i.e.,
Since BW is very very small as compare to higher cut-off frequency so the AM signal is a high frequency narrowband signal.
rad/sec
Hz

## Slide 15
For sinusoidal AM,
where
Modulation Index
Carrier
Signal
USB
LSB

## Slide 16
Frequency domain representation:-
0

## Slide 17
Power relation in AM
Carrier power
SideBand power

## Slide 18
Transmission Efficiency (or Modulation Efficiency)
It is defined as the ratio of the useful power to the total transmitted power.
Gives the percentage of useful power and the total transmitted power.
Total power,

## Slide 19
Time domain representation of AM signal

## Slide 27: Vestigial Sideband Modulation (VSB)
SSB-SC modulation is well suited for transmission of voice because of frequency gap that exist in the spectrum of voice signal zero and a few hundred Hz. When the baseband signal contains significant components at extremely low frequencies as in case of T.V. picture signal, the upper and lower side band need at carrier frequency. This means that use of SSB modulation is inappropriate for transmission of such baseband signals due to difficulty of isolating one side band.

## Slide 28: VSB
300 Hz
3300 Hz
- 3300 Hz
- 300 Hz
f
v(f)
fc+300 Hz
fc+3300 Hz
fc-3300 Hz
fc-300 Hz
f
V(f)
fc
p(f)
4.5 MHz
- 4.5 MHz
P(f)
fc+4.5 MHz
fc- 4.5 MHz
fc
f
Modulation
Modulation

## Slide 29
VSB
m()
M()
M()
In VSB Modulation, one sideband is passed almost completely where as just a trace or vestige of unwanted sideband retains.
Specifically the vestige part of unwanted sideband components for the part removed from desired sideband.
Modulation
BW =

## Slide 30
VSB
VSB Filter
Low Pass Filter
Transmitter Side
Receiver Side

## Slide 31
VSB

## Slide 33
This envelope detector consists of a diode and low pass filter. Here, the diode is the main detecting element. Hence, the envelope detector is also called as the diode detector. The low pass filter contains a parallel combination of the resistor and the capacitor.

## Slide 34: AM Receiver
Functions of Receivers
To collect the electromagnetic waves transmitted by the transmitter.
To select the desired signal and reject all others. This is known as selectivity of the receiver.
To amplify the selected modulated signal. This is known as sensitivity of the receiver.
To detect the baseband modulating signal from the modulated Radio Frequency (RF) signal.
To amplify the baseband signal so as to operate loudspeaker.
Date: 28-01-2020

## Slide 35: Definitions
Selectivity :
  The ability of receiver to distinguish between two adjacent carrier frequencies.
Sensitivity:
  The ability of receiver to detect the weakest possible signal.
  Fidelity:
  The ability of receiver to reproduce faithfully all frequency components of the baseband signal.
Notes: https://www.ques10.com/p/11434/explain-the-following-with-reference-to-radio-rece/

## Slide 36: Tuned Radio Frequency (TRF) Receiver
RF Amplifier
Demodulator
AF Amplifier
Antenna
LS
RF: Radio Frequency
AF: Audio Frequency
LS: Loud-Speaker
: Signal Frequency
Quality Factor,
AM: 535 – 1605 KHz
KHz (consider)
KHz (for 5 KHz message signal)
If KHz, to maintain the value, required is 16 KHz

## Slide 37: Superheterodyne Receiver
RF Amplifier
Mixer
IF Amplifier
Detector/ Demodulator
AF Amplifier
Local Oscillator
Ganged Tuning
LS
RF: Radio Frequency
IF: Intermediate Frequency
AF: Audio Frequency
LS: Loud-Speaker
: Signal Frequency
: Local-Oscillator Frequency
Antenna
OR
Mixer

## Slide 38: Superheterodyne Receiver
Choice of IF:
  High value of IF results in poor adjacent channel selectivity.
  Low value of IF, Image frequency rejection is poor.
  IF is fixed to 455 KHz.

## Slide 40: Superheterodyne Receiver
Problem:
For a superheterodyne receiver, the intermediate frequency is 15 MHz and the local oscillator frequency is 3.5 GHz. If the frequency of the received signal is less than the local oscillator frequency, then the image frequency (in MHz) is______________.
Given,
MHz and GHz MHz
MHz
MHz

## Slide 41: Angle Modulation
FM & PM

## Slide 43: Angle Modulation
Frequency Modulation (FM)
  In FM, the frequency of high frequency carrier signal is varied in accordance with the instantaneous value of modulating signal keeping amplitude and phase constant.
Phase Modulation (PM)
  In PM, the phase angle is varied directly in accordance with instantaneous value of modulating signal keeping amplitude and frequency constant.

## Slide 44
FM
Let m(t) -> any arbitrary modulating signal with maximum frequency
where,
PM
Let m(t) -> any arbitrary modulating signal
where,
-> frequency sensitivity in Hz/volt
-> phase sensitivity in radians/volts

## Slide 45
Relation between FM & PM
Frequency Modulator
PM Signal
Phase Modulator
FM Signal
In PM, phase angle varies linearly with whereas in FM phase angle varies linearly with the integral of .

## Slide 46
For sinusoidal FM,
Peak frequency deviation
Hence,
Modulation Index

## Slide 47
For sinusoidal PM,
Peak phase deviation,

## Slide 48
Difference between FM and PM Signal

## Slide 49
FM Modulation

## Slide 50: Problems:
A sinusoidal modulating waveform of amplitude 5 V and a frequency of 2 KHz is applied to FM generator, which has a frequency sensitivity of 40 Hz/volt. Calculate the frequency deviation and modulation index.
An FM wave is given by . Calculate the frequency deviation, modulation index, and power of FM wave.
Frequency deviation, Hz
Modulation Index,
Given,
V,
KHz = 2000 Hz,
Hz/V
Standard Equation of FM is given as,
Frequency deviation, KHz
Hz
Hz
Modulation Index,
Power of FM wave, Watts
Notes: Deviation 200, beta = 0.1
9 KHz, 200

## Slide 51: Types of frequency Modulation
Depending upon value of , there are two types of frequency modulation: Narrowband FM
and Wideband FM
1. Narrowband FM
When is very-very small
and
(1)
(2)
On putting the above values in (2),

## Slide 52
1. Narrowband FM (continue…)
The narrowband FM signal is similar to AM except that in narrowband FM,
the lower-side-band is out of phase with respect to carrier as well as upper-side-band.
Frequency domain representation:

## Slide 53
2. Wideband FM
When is large
When is large, FM produces a large number of sidebands and the bandwidth of FM is quite large.
Such systems are called wideband FM.
Here, and are periodic signals with fundamental frequency .
Thus the Fourier transform for each of these signals is an impulse train with impulses at integer multiple of and amplitude proportional to Bessel’s Function of first kind,
(1)
(2)

## Slide 54
(3)
(4)
from (2), (5), and (6),
(5)
(6)
(7)
and
2. Wideband FM (continue...)

## Slide 55
2. Wideband FM (continue...)
Frequency domain representation:
||
. . .
. . .

## Slide 56
Bandwidth for Wideband FM
rad/sec
Hz
Hz
Carson’s Rule
KHz
KHz
KHz
If 3 = KHz
Then = 75 KHz
Now,
KHz
For FM,
For PM,
KHz
KHz
KHz
If 3 = KHz
Then = 225 KHz
Now,
KHz

## Slide 57
% modulation in FM:
In FM, the % modulation is given as
% modulation =
Note: If modulation index is calculated as where KHz and KHz. Hence modulation index
becomes more than 1 (means overmodulation). Henceforth, it is given by only .

## Slide 58
Generation of FM Waves:-
There are two methods for generation of FM waves.
Direct Method:
The basic concept of FM is to vary the carrier frequency in accordance with the modulating voltage.
The carrier is generated by an ‘LC’ oscillator.
In an LC oscillator, the carrier frequency is fixed by components of tank circuit and therefore it may be varied by changing either ‘L’ or ‘C’ of tank circuit.
The oscillator whose frequency is varied is accordance with voltage (modulating signal in case of FM) is known as voltage controlled oscillator.

## Slide 59
VCO
FM signal
L
C
Variable capacitor

## Slide 60
Most LC oscillator are not stable enough to provide a carrier signal.
The carrier frequency usually fluctuates due to temperature variation, humidity, edging of the components etc.
So, instead of using the LC oscillator, a crystal oscillator may be used but since they provide highly stable carrier frequency so only a very small frequency deviation is possible.
Hence, indirect method of FM generation is preferred.

## Slide 61
Indirect Method
This method is also known as Armstrong Method.
Integrator
NBPM
Frequency
Multiplier
WBFM
Signal
Message
Signal
Crystal
Oscillator
NBFM
Signal

## Slide 62
Crystal
Oscillator
Indirect Method (continue..)
Phase
Shift
Balanced Modulator
NBFM Signal

## Slide 64
Detection of FM Waves
There are 5 methods for detection of FM Waves.
Slop Detection
Balanced Slop Detector
Foster-Seeley Discriminator
Ratio Detector
Phase Locked Loop (PLL)
Frequency selective network
Envelop detector
Amplitude
variation
FM in
Frequency
variation

## Slide 65
Phase Locked Loop (PLL)
Input
Signal
Phase Detector
Low Pass Filter
Voltage Controlled Oscillator
A PLL is essentially a feedback control system which consists 3 basic components:
Phase Detector
Low Pass Filter (LPF)
Voltage Controlled Oscillator (VCO)

## Slide 66
Working of PLL:
If an input signal of frequency is applied to the PLL, the phase detector compares the phase and frequency of incoming signal to that of the output of VCO.
If the two signals differ in frequency and/or phase, an error voltage is generated.
The phase detector is basically a multiplier and produces the sum and difference components at its output.
The high frequency component is removed by the low pass filter and the difference frequency component is then to VCO.
The signal shifts the VCO frequency in a direction to reduce the frequency difference between and .
Once this action starts, we say that the signal is in capture range.
The VCO continuous to change frequency till output frequency is exactly the same as input signal frequency, the circuit is then set to be locked.

## Slide 67
Working of PLL (continue…):
A fantastic Excel implementation of PLL and demonstration Video is available at
http://www.excelunusual.com/a-phase-locked-loop-pll-model-video-preview/
Thanks to Mr. George Lungu

## Slide 68
“Perfect locking is achieved when the signals are having same frequency and
the phase difference of between them.”
At ,
for perfect locking condition.

## Slide 69
“The low pass filter controls the capture range.”
If VCO frequency is far away, the difference frequency will be too high to pass the filter and the PLL will not respond. We say that the signal is out of capture range.
However, once locked, the filter no longer restricts the PLL and the VCO can track the signal well beyond the capture range.
“Thus locking (or tracking) range is always greater than, or at the minimum, it is equal to capture range.”

## Slide 70
Draw the waveforms of AM, FM, and PM waves for the following input signal:
Homework:

## Slide 72
Random Variables (RV)
It is numerical description of the outcome of a random experiment.
A random variable is a numerically valued function defined over a sample space.
There are two types of random variables:
Discrete Random Variable (DRV): If states only countable number of discrete values then it is called DRV.
Continuous Random Variable (CRV): If can assume any value then it is called CRV.

## Slide 73
Cumulative Distribution Function (CDF)
CDF is the probability of all possible values in the total available range.
It contains all probabilistic information of random variable and is given by
1
0.75
0.50
0.25
0
1
2
3
4
Example:
-- representing to probability

## Slide 74
Properties of CDF:
No possible event
All possible events
This property indicates that CDF is a non-decreasing function of .

## Slide 75
Probability Density(Distribution) Function (PDF)
A CRV can’t be described by any mathematical equation but we can definitely describe the probability of CRV lying within a range around any possible value by a mathematical function.
This analytical function is known as PDF and is given by

## Slide 76
Properties of PDF:
  Since CDF is always a non-decreasing function of , so its derivative will always be greater than or equal to zero.
Area under the PDF curve is always unity, i.e.,

## Slide 77
Mean or First Moment:-
Mean is a measure of where distribution is centered and is given by
Example: Find the mean of the following rectangular pulse:
represents to the expectation.

## Slide 78
Mean Square Value:-
The mean square value of a random variable is given by expectation of .
Also known as total average power
Example: Find the mean square value of the following rectangular pulse:

## Slide 79
Variance:-
It measures the spread of distribution about its mean.
The less the spread, smaller is the variance and vice-versa.
The variance of a random variable is given by

## Slide 80
Properties of expectation operation:
For Example:

## Slide 81
Problems:
Consider a random variable which is uniformly distributed between to .
Calculate (i) mean, (ii) mean square value, and (iii) variance.
2. A random variable has CDF given by .
Find:

## Slide 83
Consider a random variable with PDF given by
  Calculate the relation between and ?
Homework Problem

## Slide 84
Random Process
The time domain representation of a random variable is known as random process.
There are two types of random process:
Stationary Random Process:
  A random process is set to be stationary if its statistical properties are not the function of time.
  Statistical properties, i.e., mean, variance, autocorrelation function (ACF), etc.
  It is further of two types
  Strictly stationary random process: If the random process has same statistical property, i.e., mean, variance, autocorrelation function (ACF), etc. at any instant of time then is set to be stationary in strict sense.
  Wide sense stationary (WSS) random process: If only mean and autocorrelation function are stationary then is set to be WSS.

## Slide 85
Non-Stationary Random Process:
  A random process is set to be non-stationary if its statistical properties are the function of time.

## Slide 86
The autocorrelation function of a random process is given by
Autocorrelation Function (ACF) :-
Physical significance: The physical significance of random process is that it provides the mean of describing the independence of random process at time second apart.
It is therefore clear that more rapidly random process changes with time, more rapidly will the ACF decreases from its maximum value.
Rapidly fluctuating
random process
Slowly varying
random process

## Slide 87
Example:
Consider a random process is given by where is uniformly distributed between and . Calculate .

## Slide 88
Properties of autocorrelation function:
Correlation has its maximum value at , i.e.,
is always an even function of , i.e.,
Mean square value of a random process can be obtained from by simply putting .

## Slide 89
Ergodic Random Process
A random process is set to be ergodic
when time average of a random process becomes equal to ensemble mean.

## Slide 90
Properties of Ergodic Random Process:
The ensemble mean gives the DC component of the random process.
is the DC power of the ergodic random process.
The mean square value of a random process is the total average power of the ergodic random process.
At ,

## Slide 91
After solving, we get
Variance or
AC Power
Total Average
Power
DC Power

## Slide 92
Problem:
A stationary random process has a autocorrelation function given by
Evaluate:
Total average power
DC power
AC power
Mean
Variance
RMS value of random process (Mean square value)
= 20 + 5 + 10 = 35 W
20 W
= 5 + 10 = 15 W
15 W

## Slide 93
Power Spectral Density (PSD):
---- Power per unit BW
PSD =
Watt/rad/sec or Watt/Hz
()

## Slide 94
Properties of PSD:
or
or

## Slide 95
Gaussian/Normal PDF

## Slide 96
Central Limit Theorem:
Central Limit Theorem states that probability density of a sum of N independent random variables tends to approach a Gaussian density when the number N increases.
This theorem is applicable even when the individual random variable are not Gaussian.
For large number of N (number of samples), sum of their PDFs forms a normal (Gaussian) curve.
Maximum value of the resultant PDF can be obtained at its mean.

## Slide 97
NOISE
Noise may be defined as any unwanted form of energy tending to interfere with proper and easy reception and reproduction of wanted signal.
Depending upon whether noise is external or internal to the signal, there are two types of Noise:
External Noise: The noise which is generated externally to the system is known as external noise.
Ex.: Atmosphere Noise, Extra-terrestrial Noise, etc.
Internal Noise: The noise which is generated within the system is known as internal noise.
  Following are the types of internal noise:
  Thermal Noise – (random motion of free electrons)
  Shot Noise – (fluctuations in the number of electrons and holes)
  Partition Noise – (current has to be divided in two or more paths)
  Flicker Noise – (Low frequency noise)
  Transit-time Noise – (High )